Gear Check  - Role Card

| Equipment A tape measure Marker pen Narrow marking tape Bike Flat surface of at least 8m | Responsibilities All bikes should be checked prior to the event and the first three riders plus any picked at random should be rechecked as soon as the event finishes. If a bike does not meet the regulations the rider will be disqualified. |
| --- | --- |

How to check gears

A roll out is the technique used to check whether a bike is within the regulations. The maximum gear restriction is the distance the bike travels in a straight line through one full revolution of the cranks, when in the biggest gear available on the bike. See table below.

| Category | Road Racing | Track Racing | Roller Racing |
| --- | --- | --- | --- |
| Junior U18 | 7.93m | n/a | n/a |
| Youth A U16 | 6.93m | 6.93m | 7.33m |
| Youth B U14 | 6.45m | 6.45m | 7.4m |
| Youth C U12 | 6.05m | 6.05m | 6.94m |
| Youth D U10 | 5.4m | 5.4m | 5.4m |
| Youth E U8 | 5.1m | 5.1m | 5.1m |

Performing a roll out

- Lay a straight line of tape out to 8m

- Mark the distance for the relevant categories out and make sure they are easily distinguishable.

- Ensure the bike is in its highest configuration and that the gears are engaged correctly.

- Make sure the chain is engaged in the smallest possible rear sprocket and take all the slack out of the bike.

- Position the bike at the starting point on the rollout, ensure that the crank is in bottom dead centre position and aligned with the zero point on the measure.

- Roll the bike backwards, ensuring to stay in a straight, following the marked area.

- Stop the bike once the crank has completed a full revolution and the crank is back at bottom dead centre.

- Assess whether the crank is within or over the gear restrictions relative to the distances marked out.

Bikes can be restricted to a lower gear. To do this you need to adjust the limit screw on the rear derailleur. This will prevent the chain dropping onto the smaller sprockets; this can also be done with the front derailleur to restrict the big chain ring if required.